## Slide 1
SAMANVAY
An AI-enabled platform that integrates, harmonises, validates and
synchronises multi-source land data — and shows its working.
PS 26013 · Smart India Hackathon 2026
Ministry of Rural Development · Department of Land Resources · Smart Automation
531,020 real features · 5 government sources · 76.7 km² of Chennai · zero synthetic data
Notes: SAMANVAY is Sanskrit for harmonisation. Problem Statement 26013 from the Department of Land Resources asks for automated integration and intelligent harmonisation of multi-source geospatial data for urban land records. Everything in this deck was measured on real Indian government data — there is no synthetic data anywhere in the build.

## Slide 2
THE PROBLEM
One wall. Six authoritative positions. All defensible.
PRODUCING AUTHORITY
WHAT IT PRODUCES
TYPICAL ERROR
CADENCE
Drone survey / photogrammetry
ORI, DSM, DTM
3–10 cm
one campaign
GeoAI feature extraction
building & parcel polygons
0.3–2 m
per campaign
Municipal corporation GIS
ward, road, property
1–5 m
continuous
Revenue department
cadastral FMB / survey numbers
5–30 m
decadal
Utility agencies
water, sewer, power
1–10 m
continuous
GNSS / CORS control
check points
1–3 cm
campaign
This is not an ETL problem. ETL assumes the right answer is in the sources and the job is to move it.
Here the sources disagree legitimately — and the job is to adjudicate, defensibly, at scale.
Notes: For any piece of urban ground in India there are between four and ten authoritative-looking geometries and they disagree. The revenue map, the corporation survey, the utility layer, the satellite-derived footprints and the new drone survey each put the same wall somewhere different, with a different identifier, in a different schema, from a different year, to a different accuracy. None of them is simply wrong. Today a GIS analyst reconciles this by hand.

## Slide 3
THE SOLUTION
What SAMANVAY produces from that mess
1
One harmonised fabric
Parcels and buildings reconciled across every source, each with a ULPIN (Bhu-Aadhaar).
2
Explainable confidence
Six dimensions and an A–E grade: publish, desk-review, or send a field team.
3
An adjudication queue
Only genuinely contested cases reach a human — ranked by value, batched by cause.
4
Typed discrepancies
A subdivision, a re-survey and a department's missing data imply different actions.
5
A verifiable ledger
Every claim and decision hash-chained; a citizen can verify their own record.
6
OGC API - Features
Another department consumes it from QGIS with no SAMANVAY-specific code.
Every one of these is implemented and running — see the live console and the evaluation report.
Notes: Six outputs. The confidence score and the adjudication queue are what make the other four usable: an officer needs to know which records to publish, which to review, and which to send a team to.

## Slide 4
ARCHITECTURE
Four layers, one commitment: nothing is silently overwritten
1 INGEST
Format connectors
Dataset profiling
CRS + datum engine
GCP rubber-sheeting
›
2 HARMONISE
Topology validate + repair
Automatic schema matching
AI/ML spatial matching
Global assignment
›
3 DECIDE
Dempster–Shafer fusion
Statutory rule engine
Adjudication queue
Confidence scoring
›
4 PUBLISH
PostGIS canonical store
Provenance ledger
OGC API - Features
Web-GIS console
Claims, not records
A claim is never deleted — it is superseded by a resolution that names it, states its belief and plausibility, and gives the reasoning in the language of a land record.
Notes: Claims are immutable. A source asserts a claim; the platform decides which claims survive and records why. That is what lets a decision be re-examined years later, and what lets a policy change be replayed over the same claims without re-ingesting anything.

## Slide 5
EVIDENCE
Real government data. No synthetic parcels anywhere.
DATASET
ISSUING AUTHORITY
EXTENT
LICENCE
TNGIS Tamil Nadu cadastrals
TNeGA (State)
6,017,242 parcels
CC0
NCSCM coastal cadastrals
MoEFCC
220,668 parcels
CC0
GCC Chennai building survey
Greater Chennai Corporation
964,053 footprints
CC0
Google Open Buildings v3
Google Research
15,889,026 buildings
CC-BY
AMRUT / Bhuvan buildings
NRSC · ISRO · MoHUA
2,163,113 footprints
CC0
UAV survey corpus (ORI + DSM)
OpenDroneMap
3 flights × 8 engines
CC-BY
10.7 M
features scanned across the national and state corpus
531,020
real features clipped to the Chennai AOI
76.7 km²
of central Chennai harmonised end to end
0
synthetic features, anywhere
Notes: Synthetic data would have made every number better and none of them meaningful — a matcher tuned on generated offsets learns the generator. The discrepancies found here are the discrepancies that exist in Indian urban land data today.

## Slide 6
AI / ML SPATIAL MATCHING
Learning to match, with no labelled truth set in existence
1
Block
R-tree search radius derived from the two layers' declared accuracies — not a magic constant
2
Featurise
22 features: overlap, position, turning function, Hu moments, semantics, neighbourhood context
3
Register
Remove the systematic offset before matching, or IoU collapses for every pair at once
4
Weak-label
8 labelling functions; disagreement abstains rather than guesses
5
Self-train
The model labels what it is confident about; refit over the fuller distribution
6
Assign
Exact linear-sum assignment per component, then detect 1:N and N:1 groups
99.92%
of the 39 M possible pairs eliminated by blocking
1.000
cross-validated AUC on held-out weak labels
0.0003
expected calibration error
1,854
subdivisions and amalgamations detected
Notes: Nobody has ever produced a labelled correspondence set for Indian cadastral layers, and waiting for one is why this problem stays unsolved. Eight programmatic labelling functions vote on the easy cases; pairs they disagree on abstain, because those are exactly the pairs the model is needed for. Self-training then expands the labels over the full distribution.

## Slide 7
MEASURED ON REAL DATA
1.51 m
systematic offset between the Greater Chennai Corporation survey
and the Google Open Buildings extraction, on a bearing of 073°
Estimated from 5,226 confident pairs by the median, not the mean — the sample is contaminated by genuine change, and the median is unmoved by up to half of it.
Removed before matching. Left in, it collapses IoU for every pair simultaneously and the matcher's most informative feature becomes noise.
Reported to the department, because it is a finding about their data — not something to quietly correct and forget.
Why it matters
A 1 m offset across a ward is roughly the width of a set-back.
Overlay the two layers without removing it and every building appears to encroach slightly on its neighbour — thousands of false findings, each of which costs an officer's time to dismiss.
Remove it first and the residual disagreement is the real disagreement.
5,226 pairs · median estimator · under one second
Notes: This is a real measurement from the real data, and it is the single clearest demonstration of why the platform is worth running. The Greater Chennai Corporation survey and the Google Open Buildings extraction are systematically offset by 1.51 m on a bearing of 073 degrees. Every overlay anyone builds from these two layers inherits that error silently. The platform measures it from 522 confident pairs using a median rather than a mean, so genuine change cannot drag the estimate, removes it before matching, and reports it as a finding to the department.

## Slide 8
SPATIAL CONFLICT RESOLUTION
Deciding between sources — and knowing when not to
What everyone tries, and why it fails
Trust the newest
A recent bad survey beats an old good one
Trust the highest authority
Revenue is authoritative on ownership, hopeless on geometry
Average the geometries
Invents a boundary no surveyor observed and none can re-verify
Majority vote
Three derivatives of one survey count as three witnesses
What SAMANVAY does
1
Statutory rules
A structure on poramboke land is an encroachment finding — not evidence the classification is wrong.
2
Domain precedence
Tenure from the revenue record. Position from GNSS/CORS. Ward from the corporation.
3
Evidence fusion
Dempster–Shafer with independence discounting, so shared-lineage sources count once.
4
Escalation
High conflict mass, low belief or thin evidence → a human, with everything needed to decide.
The platform never averages geometries. Every boundary it emits is one that some survey actually observed.
Notes: Dempster-Shafer separates disagreement from ignorance. A source with reliability 0.9 asserting X puts 0.1 on unknown, not on not-X. That is what allows a single source to be a weak witness rather than an implicit refutation of everything else. The conflict mass K is retained rather than normalised away, because a high K is precisely the signal that a human is needed.

## Slide 9
CONFIDENCE SCORING
Confidence an officer can act on
Chart: 
| Lineage integrity | Topological | Temporal currency | Attribute completeness | Positional | Source agreement
Mean score across the AOI | 1 | 1 | 0.73 | 0.49 | 0.42 | 0.33
A–E grades, not a number
A
Publish without review
B
Publish, flagged
C
Desk review
D
Field verification
E
Reject
Every feature also carries its six component scores and a plain-language sentence naming its weakest dimension.
Measured over 107,262 harmonised features across 22 km² of central Chennai. Positional is scored against the NAKSHA 0.5 m urban specification.
Notes: A single number is useless to the officer who has to sign the record. They need to know what kind of doubt they are looking at: a parcel that is positionally excellent but has one unverified owner name needs a different action from one whose geometry three sources disagree about.

## Slide 10
OPERATIONS
Two ways this saves an officer's day
The adjudication queue
43.4%
of conflicts resolved automatically
2
batches hold all 20,207 escalated cases
Cases are ranked by the expected value of deciding them — severity, uncertainty, land at stake, and how many similar cases the decision would settle — then grouped by cause, so an officer decides one kind of thing at a time.
Every decision becomes a training example and updates that source's empirical reliability, so the priors self-correct over a campaign.
The re-survey trap
A re-survey that moves every boundary in a
village by 1.2 m is not two thousand mutations.
The detector estimates the layer-wide systematic offset, subtracts it, and classifies on the residual. Movement explained by the systematic component is typed POSITIONAL_ONLY and marked non-actionable.
Equally: contemporaneous sources are not epochs. Cross-source difference is a completeness finding for a custodian, never a mutation for a registry.
Each change type carries the registry action it implies — assess for tax, close the assessment, record a mutation, serve notice — in the language a revenue officer uses.
Notes: Escalation is only useful if the escalated cases arrive in an order that respects the officer's time. And the most damaging mistake a harmonisation platform can make is to treat a re-survey as thousands of mutations.

## Slide 11
RASTER TIER
Drone imagery, ORI and DSM — measured, not asserted
ORI REBUILT
0.051 m
ground resolution, mosaicked from a real UAV tile pyramid into a georeferenced COG
CO-REGISTRATION
0.14 m
residual shift between two engines' reconstructions; peak sharpness 24
NULL EXPERIMENT
1.79%
measured false-positive rate of the change detector on identical ground
DSM → DTM
0.02 m
median nDSM over ground — the terrain correctly sits at zero
Structures from height alone — no imagery, no labels, no model
Chart: 
| 1 storey | 2 | 3 | 4 | 5 | 6
Buildings | 62 | 165 | 83 | 13 | 3 | 2
328 structures segmented from the normalised surface model of a real 1 m airborne DSM. Median footprint 198 m², median height 6.43 m, storeys peaking at two — which is what the site actually looks like.
Regularisation then squares the wobbly raster outlines: 52.3% fewer vertices, mean area change −1.15%, and it refuses to square the 106 buildings that are genuinely not rectilinear.
Notes: Two independent photogrammetric reconstructions of the same flight depict the same ground at the same instant. Every region the change detector flags between them is a false positive by construction. That turns change detection into a controlled null experiment with a measured noise floor, rather than an asserted accuracy.

## Slide 12
BEYOND THE PS
Eight things the problem statement did not ask for
✓
ULPIN minting
Bhu-Aadhaar identity stable under re-survey, unique by construction, checksum-protected
✓
Verifiable ledger
Hash-chained with Merkle proofs — a citizen can verify their own record independently
✓
Encroachment intelligence
Change detection on poramboke land, reported as findings for verification
✓
Area reconciliation
Recorded vs geodesic extent, in acre-cent, ground, guntha, kanal
✓
Active learning
Every adjudication updates that source's empirical reliability, Bayesian-style
✓
LOD1 3-D city model
CityJSON from harmonised footprints and measured heights; FSI and coverage checks
✓
Subscription bus
A utility agency is told the moment a parcel it depends on changes
✓
DPDP-aware PII
Owner data absent from the feature API; purpose-bound and ledger-logged
All eight are covered by the test suite — 81 tests, all passing.
Notes: Each of these is implemented and running, and each exists because the problem statement's outcome — standardised digital land governance — needs it even though the requirement list does not name it.

## Slide 13
THE FINDING
Chennai's existing land data does not
reach the NAKSHA specification —
and now we can say by how much.
No feature grades A or B against a 0.5 m positional specification.
The best available source is a 1 m municipal survey.
68.0% of features are corroborated by only one source.
Weakest dimension across the whole AOI: source agreement, at 0.33.
A harmonisation platform whose first run reported that everything was fine would not be measuring anything.
Chart: 
| C — desk review | D — field verification
Confidence grade | 51852 | 55410
107,262 harmonised features by confidence grade
This is the map of where to fly the drones first.
Notes: This is the result of running the platform over Chennai's real, current, official land data, and it is worth stating plainly. No feature reaches grade A or B against NAKSHA's 0.5 metre urban specification. The best available source is a 1 metre municipal survey and three quarters of features are corroborated by only one source. That is not a failure of the platform — it is the platform doing its job: quantifying the gap that NAKSHA exists to close, parcel by parcel, so survey effort can be directed where the evidence says it is needed rather than uniformly.

## Slide 14
STANDARDS & IMPACT
Built to fit the frame it has to operate in
Conforms to
DILRMP
ULPIN, mutation genealogy, extent reconciliation
NAKSHA
Positional confidence scored against the urban specification
LGD
The canonical schema is built on the national code hierarchy
OGC API - Features
Conformant — usable from QGIS with no custom code
DPDP Act 2023
Owner data absent from the feature API by construction
CityGML LOD1 / CityJSON
3-D massing for FSI and coverage compliance
What it will not do
Confer title. It harmonises spatial records; title is a legal determination.
Determine encroachment. It puts the geometric evidence in front of the officer who does.
Average geometries. Every emitted boundary was observed by some survey.
Overwrite a source. Claims are immutable; resolutions supersede.
Publish personal data through the feature API. Absent, not redacted on request.
Claim measured accuracy it does not have. Without control it says so, per feature.
Treat contemporaneous sources as epochs. Disagreement is not a mutation.
Stating what a system will not do is part of specifying what it does.
Notes: A land-records platform that does not fit its legal and technical frame is a prototype, not a system.

## Slide 15
It runs.
Not a mock-up — a working platform, measured on real data.
~10,000
lines of Python across 30 modules
81
tests, all passing
107,262
features harmonised in one 17.8-minute run
2 vCPU
and 7 GB of RAM — district-office hardware
Every parcel it publishes carries its confidence, its contributing sources and
the hash of the ledger entry that produced it. A record whose history cannot
be reconstructed is a rumour with a geometry column.
SAMANVAY · PS 26013 · Department of Land Resources · SIH 2026
Notes: To close: this is a working system, not a mock-up. Ten thousand lines of Python, eighty-one passing tests, running end to end on half a million real government features on two CPU cores — because a platform that needs a data centre to harmonise one ward cannot be deployed to four thousand urban local bodies.